## Slide 1: Noise and image acquisition + Panoramas
Fredo Durand
MIT EECS
6.815/6.865

## Slide 2: Noise characteristics

## Slide 3: Analyzing noise
Camera on tripod, many pictures
Compute mean, variance, stddev, SNR

## Slide 4: Exposure
Get the right amount of light to sensor/film
Two main parameters:
  Shutter speed
  Aperture (area of lens)
+ sensor sensitivity (ISO)
In what follows, I kept the brightness the same and explored the tradeoff between shutter speed and ISO

## Slide 5: Analysis code
def analyzeNoise(imSeq):
mean=imSeq[0].copy()
N=len(imSeq)
for i in xrange(1, N):
mean+=imSeq[i]
mean/=N
variance=zeros(imSeq[0].shape)
for i in xrange(N):
diff=imSeq[i]-mean
variance+=diff*diff
variance/=N-1
return mean, variance

## Slide 6: Canon 1D mark IIN at ISO 3200

## Slide 7: Canon 1D mark IIN at ISO 3200

## Slide 8: Canon 1D mark IIN at ISO 3200
Looks noisy, especially in dark areas

## Slide 9: Canon 1D mark IIN at ISO 3200
Denoised with 45 images (estimator of mean)

## Slide 10: Canon 1D mark IIN at ISO 3200
Standard deviation (some alignment issues...)
For each pixel, for each channel, compute
And display as an image

## Slide 11: Canon 1D mark IIN at ISO 3200
Standard deviation (some alignment issues...)
Observations:
more noise in bright image areas

## Slide 12: Canon 1D mark IIN at ISO 3200
Standard deviation (some alignment issues...)

## Slide 13: Canon 1D mark IIN at ISO 3200
log SNR -- looks a lot like the image!

## Slide 14: Canon 1D mark IIN at ISO 3200
log SNR -- looks a lot like the image!
even though we have more noise, bright areas have better SNR

## Slide 15: Observations
Noise is more visible in dark areas
Noise is numerically higher in bright areas
SNR is better in bright areas

## Slide 16: Canon 1D mark IIN at ISO 3200

## Slide 17: Canon 1D Mark II, ISO 100
Lot less noisy!

## Slide 18: Canon 1D mark IIN at ISO 3200
Standard deviation (some alignment issues...)

## Slide 19: Canon 1D Mark II at ISO 100
Standard deviation (some alignment issues...)

## Slide 20: Canon 1D mark IIN at ISO 3200
log SNR

## Slide 21: Canon 1D mark IIN at ISO 1600
log SNR

## Slide 22: Canon 1D mark IIN at ISO 400
log SNR

## Slide 23: Canon 1D mark IIN at ISO 100
log SNR

## Slide 24: Nikon D3s at 1600 ISO

## Slide 25: Nikon D3s at 1600 ISO

## Slide 26: Canon 1D Mark IIN at 1600 ISO

## Slide 27: Check stationarity

## Slide 28: Distribution of individual pixels
Show histogram at a given pixel

## Slide 29: Changing the camera

## Slide 30: Recap and questions?
Noise level depends on
  pixel intensity
  ISO
  color channel
  camera

## Slide 31: Noise Origin

## Slide 32
FROM PHOTONS TO PIXELS & NOISE

## Slide 33: What limits camera dynamic range
Saturation for bright pixels
Noise for dark pixels

## Slide 34: Noise!
http://en.wikipedia.org/wiki/File:Highimgnoise.jpg

## Slide 35: Digital pipeline
Photosites transform photons into charge (electrons)
  The sensor itself is linear
Gets amplified (depending on ISO setting)
Then goes through analog to digital converter
  up to 14 bits/channel these days
Stop here when shooting RAW
Then demosaicing, denoising, white balance, a response curve, gamma encoding are applied
Quantized and recorded as 8-bit JPEG

## Slide 36: Pipeline & noise
This is a conceptual diagram, don’t take it too literally
  e.g. the AD converter is a serious source of noise, but usually electronic noise, not quantization artifacts
Orders of magnitude:
  # of photons per photosite : 10,000-100,000
  Electronic noise 5-30 electrons per photosite
Sensor
Gain (ISO)
A/D
Photon
noise
additive
noise
additive
noise
quantization
Photons
Digital image

## Slide 37: ISO amplifies
e.g. going from ISO 100 to ISO 400 amplifies by 4
both noise & signal
usually use high ISO when signal is low => worse signal/noise ratio
Sensor
Gain (ISO)
A/D
Photon
noise
additive
noise
additive
noise
quantization
small #
Photons
Digital image

## Slide 38: Canon 1D mark IIN at ISO 3200

## Slide 39: Canon 1D Mark II, ISO 100
Lot less noisy!

## Slide 40: ISO
http://en.wikipedia.org/wiki/File:ISO_comparison_150px.jpg
ISO 100
ISO 1600
Canon 400D

## Slide 41
http://wiegaertnerfilms.com/tutorials/the-best-iso-settings-for-canon-video-dslrs/

## Slide 42
http://gizmodo.com/5470334/giz-explains-why-iso-is-the-new-megapixel
http://www.sansmirror.com/articles/proper-noise-reduction-in.html

## Slide 43: ISO
But, for a given signal level, and a given desired image brightness,
Sensor
Gain (ISO)
A/D
Photon
noise
additive
noise
additive
noise
quantization
small #
Photons
Digital image

## Slide 44: ISO
But, for a given signal level, and a given desired image brightness, two alternatives
  use low ISO and brighten digitally
  use high ISO to get brightness directly
The latter gives less noise because you don’t amplify post-gain noise
Sensor
Gain (ISO)
A/D
Photon
noise
additive
noise
additive
noise
quantization
small #
Photons
Digital image

## Slide 45: ISO recap
ISO is a simple gain
amplifies noise as well
But when the signal is low, it’s better to amplify as early as possible (ISO rather than digitally)
Ideally, you make sure the signal is high by use a slower exposure or larger aperture

## Slide 46: Modern ISO is confusing
Sometimes analog gain, sometimes digital
Some modern cameras are close to iso-invariant (brightening digitally an under-exposed image in post is equivalent to using a high ISO)
  https://photographylife.com/iso-invariance-explained
  https://improvephotography.com/34818/iso-invariance/
  http://www.photonstophotos.net/Charts/RN_ADU.htm
  https://www.dpreview.com/reviews/image-comparison/fullscreen?attr134_0=canon_eos5d&attr134_1=canon_eos5d&attr134_2=canon_eos5d&attr134_3=canon_eos5d&attr136_0=1&attr136_1=1&attr136_2=3&attr136_3=2&normalization=full&widget=487&x=0.151173145&y=0.5005349

## Slide 47: Questions?

## Slide 48: Main noise sources
Quantum (aka Schott/shot/Poisson/photon) noise
  Statistical fluctuation of # photons
Additive electronic noise
  read noise: before amplification => worsens with higher ISO
  after amplification (at ADC level in particular) => same for all ISO
Sensor
Gain (ISO)
A/D
Photon
noise
additive
noise
additive
noise
quantization
Photons
Digital image

## Slide 49: Main noise sources
Quantum (aka Schott/shot/Poisson/photon) noise
  Statistical fluctuation of # photons
Additive electronic noise
  read noise: before amplification => worsens with higher ISO
  after amplification (at ADC level in particular) => same for all ISO
Misc.
  thermal (mostly for long exposure)
  various fixed pattern issues

## Slide 50: Photon noise
Say the average flux of Photons over the sensor is, 100 photons during the exposure time
  With random fluctuation, we might get 96, or maybe 101, maybe 105.
Extreme case: the average flux is 0.5 photons during the exposure:
  We might get 0 or 1
The amount of fluctuation grows with the average rate, but not as fast: square root.
  absolute noise increases with intensity
  relative noise decreases
clarkvision.com

## Slide 51: Photon noise (simulation)
Going from left to right, the mean number of photons per pixel over the whole image is (top row) 0.001, 0.01, 0.1 (middle row) 1.0, 10.0, 100.0
http://en.wikipedia.org/wiki/File:Photon-noise.jpg

## Slide 52: Great ref on noise
http://theory.uchicago.edu/~ejm/pix/20d/tests/noise/index.html
Noise, Dynamic Range and Bit Depth in Digital SLRs
by Emil Martinec © 2008

## Slide 53: Canon 1D mark IIN at ISO 3200
log SNR - dominated by Poisson, ~sqrt(image)

## Slide 54: Overall Signal Noise Ratio
http://www.clarkvision.com/imagedetail/digital.sensor.performance.summary/

## Slide 55: Sensor size varies a lot and influences noise
0
http://www.photozone.de/3Technology/digital_1.htm

## Slide 56: Well capacity & pixel size
Well capacity: max number of electro per photosite
Bigger pixel is better:
  reduce Photon noise
  increase electronic signal, need less gain
http://www.clarkvision.com/imagedetail/digital.sensor.performance.summary/

## Slide 57
Photometric limits for digital camera systems
punchline: we’re pretty close to the physical limits, noise is dominated by the number of photons
http://electronicimaging.spiedigitallibrary.org/article.aspx?articleid=1199156

## Slide 58: Thermal noise (long exposures)
Thermal noise in 20D blackframes at ISO 400. The knee in the data at exposure time 15sec is due to the max pixel raw level reaching 4095
(the maximum possible value on this camera), indicating that the rise in standard deviation is largely due to a few outlyers in the distribution.
http://theory.uchicago.edu/~ejm/pix/20d/tests/noise/index.html

## Slide 59: Pre vs. post gain noise
Note: ADC noise here means additive electronic noise after the gain, it is not quantization error
Note: the signal also decreases with higher ISO
http://www.clarkvision.com/imagedetail/digital.sensor.performance.summary/

## Slide 60: Recap: Main noise sources
Quantum (aka Schott/shot/Poisson/photon) noise
  srqt(#photons)
  dominates for brighter pixels
Additive electronic noise
  read noise: before amplification => worsens with higher ISO
  after amplification (at ADC level in particular) => same for all ISO
  usually dominates for dark pixels
Misc.
  thermal (mostly for long exposure)
  various fixed pattern issues

## Slide 61: Different regimes
For bright pixels (in fact, most pixels), photon noise dominates
For dark pixels: electronic noise dominates
For low ISO, post-gain noise dominates
For high ISO, pre-gain noise dominates
For long exposures, thermal noise kicks in

## Slide 62: Factors that influence noise
Pixel pitch (8 microns: good, 2 microns: bad)
Area of the photosite actually photosensitive
Microlens that focus light on that photosensitive area
Quality of electronics
  Analog to Digital converter, power supply
Temperature
  CCDs for Astronomy are cooled

## Slide 63: Read noise (before gain)
http://www.clarkvision.com/imagedetail/digital.sensor.performance.summary/

## Slide 64: Pipeline & noise
Orders of magnitude:
  # of electrons per photosite : 10,000-100,000
  Electronic noise 5-30 electrons per photosite
Shot noise: sqrt(#photons)
  Shot noise ~100 -300 for bright value
  shot noise of 10 <-> 100 photons
Sensor
Gain (ISO)
A/D
Photon
noise
additive
noise
additive
noise
quantization
Photons
Digital image

## Slide 65: Response curve, dynamic range
Video sensors have poor dynamic range

## Slide 66: Questions?

## Slide 67: Dynamic range and sensor size
http://www.dpreview.com/news/0011/00111608dynamicrange.asp

## Slide 68: Noise & quantization
Note: quantization is NOT the limiting factor. Instead, the well capacity and noise are.
  14 bits does not necessarily mean more dynamic range than 12 bits

## Slide 69: Questions

## Slide 70: Digital sensors are awesome
Nikon D3s at f/2.8, 8 sec at ISO 6400

## Slide 72: Brain teaser
For the same light level and electronic (per photosite read noise), and same total sensor size, is it better to:
  have a 16 Mpixel sensor and average groups of 4 pixels to yield a 4 Mpixel image
  have a 4Mpixel sensor (with bigger photosites)
Analyze Photon noise and read noise.

## Slide 73: Brain teaser 2
One long exposure
multiple shorter exposures

## Slide 74: Histogram
See http://www.luminous-landscape.com/tutorials/understanding-series/understanding-histograms.shtml http://www.luminous-landscape.com/tutorials/expose-right.shtml
Horizontal axis is pixel value
Vertical axis is number of pixels

## Slide 75: Highlights
Clipped pixels (value >255)
Pro and semi-pro digital cameras allow you to make them blink.

## Slide 76: Recap: Digital photography pipeline
Photosites transform photons into charge (electrons)
Gets amplified (depending on ISO setting)
Analog to digital converter
Stop here when shooting RAW
Demosaicing
Denoising
Color space conversion (from sensor to sRGB)
White balance
Response curve, color enhancement
Gamma encoding
Quantized and recorded as JPEG
  DCT, quantization based on CSF, entropy coding
Well, some cameras apply some processing such as denoising to the RAW data

## Slide 77: Recap: Digital photography pipeline
Photosites transform photons into charge (electrons)
Gets amplified (depending on ISO setting)
Analog to digital converter
Stop here when shooting RAW
Demosaicing
Denoising
Color space conversion (from sensor to sRGB)
White balance
Response curve, color enhancement
Gamma encoding
Quantized and recorded as JPEG
  DCT, quantization based on CSF, entropy coding
Well, some cameras apply some processing such as denoising to the RAW data

## Slide 78: Response curve of D-SLR
straight for mid-tones
toe and shoulder preserve more dynamic range around dark and bright areas, at the cost of reduced contrast
  http://www.dpreview.com/reviews/canoneos5d/page22.asp

## Slide 79: ETR

## Slide 80: Non-linearities

## Slide 81: Non-linearities at the end
We don’t exactly observe the true value plus a zero-mean noise
Because of sensor non-linearities: clamped at 0 and max
Consequence:
  Denoising by averaging can give dark regions that are too bright
Canon trick: they add a constant offset to the sensor signal to make sure the noise is zero-mean

## Slide 82: Other approaches to denoising

## Slide 83: Denoising
Bayesian coring in the wavelet domain
  Simoncelli & Adelson
Big heuristics
  BM3D
NL means
  Buades et al.
  Bilateral in the space of patches
Statistics of natural images
Limits of denoising
  http://www.wisdom.weizmann.ac.il/~levina/

## Slide 84: References

## Slide 85
http://www.cambridgeincolour.com/tutorials/image-noise.htm
http://www.cambridgeincolour.com/tutorials/image-noise-2.htm
http://www.clarkvision.com/imagedetail/does.pixel.size.matter2/
http://www.clarkvision.com/articles/digital.sensor.performance.summary/
http://books.google.com/books?id=OYFYt5C4N94C&pg=PA405&dq=binomial+film+grain+noise#v=onepage&q=binomial%20film%20grain%20noise&f=false
http://en.wikipedia.org/wiki/Image_noise
http://www.picturecode.com/noise.htm
http://www.instructables.com/id/Avoiding-Camera-Noise-Signatures/
http://www.photoxels.com/tutorial_noise.html
http://people.csail.mit.edu/hasinoff/hdrnoise/hasinoff-sensornoise-tutorial-iccp10.pptx
http://theory.uchicago.edu/~ejm/pix/20d/tests/noise/
http://www.imatest.com/docs/noise/
http://www.cambridgeincolour.com/tutorials/image-averaging-noise.htm
http://www.petapixel.com/2012/02/21/a-simple-explanation-of-how-iso-works-in-digital-photography/

## Slide 86: Panoramas

## Slide 87: Applied homographies
http://vimeo.com/75260457

## Slide 88: Applied homographies
http://vimeo.com/75260457

## Slide 89
Astronomy
White board rectification
http://www.astronomie.be/registax/

## Slide 90
Fredo office hours?

## Slide 91: Panoramas and Homographies
Fredo Durand
MIT EECS 6.815/6.865

## Slide 92: Piaza

## Slide 93: Motivation

## Slide 94: Panorama: virtual wide angle

## Slide 95: All the way to 360
http://people.csail.mit.edu/fredo/Panos/

## Slide 96: Why Mosaic?
Are you getting the whole picture?
  Compact Camera FOV = 50 x 35°
  Human FOV = 200 x 135°
Slide from Brown & Lowe

## Slide 97: Why Mosaic?
Are you getting the whole picture?
  Compact Camera FOV = 50 x 35°
  Human FOV = 200 x 135°
  Panoramic Mosaic = 360 x 180°
Slide from Brown & Lowe

## Slide 98: Similar to HDR
Medium is limited (range, field of view)
Take multiple images
Merge

## Slide 100: An old idea
This image by the firm of Maison Bonfils depicts the city of Beirut, Lebanon, sometime in the last third of the 19th century. Maison Bonfils was the extraordinarily prolific venture of the French photographer Félix Bonfils (1831-85), his wife Marie-Lydie Cabanis Bonfils (1837-1918), and their son, Adrien Bonfils (1861-1928). The Bonfils moved to Beirut in 1867 and, over the next five decades, their firm produced one of the world's most important bodies of photographic work about the Middle East. Maison Bonfils was known for landscape photographs, panoramas, biblical scenes, and posed “ethnographic” portraits. The family’s marketing acumen and commercial sense helped make their photographs known around the world. “Panoramic” photographs employ a variety of techniques to create a wide angle of view. This “panoramic view” is composed of four aerial photographs set together to give the viewer a broader image than would have been practical with a single photograph. http://en.wikipedia.org/wiki/File:%D8%A8%D9%8A%D8%B1%D9%88%D8%AA-%D8%A7%D9%84%D9%82%D8%B1%D9%86_%D9%A1%D9%A9.jpg
http://en.wikipedia.org/wiki/File:%D8%A8%D9%8A%D8%B1%D9%88%D8%AA-%D8%A7%D9%84%D9%82%D8%B1%D9%86_%D9%A1%D9%A9.jpg

## Slide 101: An old idea
http://en.wikipedia.org/wiki/File:Panorama_of_Tiflis_(1900s).jpg
http://en.wikipedia.org/wiki/File:%D8%A8%D9%8A%D8%B1%D9%88%D8%AA-%D8%A7%D9%84%D9%82%D8%B1%D9%86_%D9%A1%D9%A9.jpg

## Slide 102: Old panos, modern viewer
http://www.eurofresh.se/history/

## Slide 103: 19th century panorama

## Slide 104: Traditional panoramas

## Slide 105
http://www.kaidan.com/products/pano-prods.html
http://www.0-360.com/
http://www.bugeyedigital.com/product_main/036-0360d.html
http://www.panoramicphoto.com/timeline.htm

## Slide 106: Overview

## Slide 107: Today
The user gives us 4 correspondences
We reproject one image to match the other one
Creates a wider angle view

## Slide 108: Later
Automagic correspondences
  corner detection
  patch descriptor
Nice blending
  smooth transition
  2 scale

## Slide 109: Overview
Today: Manual panorama
  perspective and image reprojection
  Homogenous coordinates and homographies
  Inferring homography from correspondences
Automatic panorama
Nice blending

## Slide 110: Spoiler
It’s all a 3x3 matrix + division
p
p’
H

## Slide 111: Reprojection

## Slide 112: Virtual wide angle
Take N images in different directions
Deduce the image that would have been taken by a wider angle lens
…but wait, why should this work at all?
  What about the 3D geometry of the scene?
  Why aren’t we using it?

## Slide 113: Simplified projection model

## Slide 114: A pencil of rays contains all views
real
camera
synthetic
camera
Can generate any synthetic camera view
as long as it has the same center of projection!
viewpoint

## Slide 115: Entrance pupil
When camera is rotated around entrance pupil , there is no parallax
  That is, if two 3D points are superimposed for one orientation, they remain superimposed after rotation
Finding the entrance pupil is painful
  and it’s often incorrectly called nodal point
  http://www.reallyrightstuff.com/pano/index.html
  http://www.path.unimelb.edu.au/~bernardk/tutorials/360/photo/nodal.html

## Slide 116: Recap
When we only rotate the camera (around nodal point) depth does not matter
It only performs a 2D warp
  one-to-one mapping of the 2D plane
  plus of course reveals stuff that was outside the field of view
Now we just need to figure out this mapping
real
camera
synthetic
camera

## Slide 117: Other interpretation
Depth does not matter
We can pretend that each pixel is at a convenient depth
viewpoint
  Three convenient depth distributions:
    spherical
    planar
    cylindrical
  We focus on planar
    it makes life more linear
    Still useful for spherical panos

## Slide 118: Question?

## Slide 119: Aligning images
  We have established that pairs of images from the same viewpoint can be aligned through a simple 2D spatial transformation (warp).
  What kind of transformation?

## Slide 120: Aligning images: translation
  Translations are not enough to align the images
left on top
right on top

## Slide 121: Back to Image Warping
Affine
6 unknowns
Perspective
8 unknowns
Which transform is the right one for warping Projection Plane PP1 into Projection Plane PP2?
e.g. translation, Euclidean, affine, projective
Translation
2 unknowns

## Slide 122: Image reprojection: back to 3D
mosaic PP
The mosaic has a natural interpretation in 3D
  The images are reprojected onto a common plane
  The mosaic is formed on this plane
  Mosaic is a synthetic wide-angle camera

## Slide 123: Recap
We are looking for the 2D mapping that corresponds to a 3D rotation of the camera
We need to understand perspective projection

## Slide 124: Spoiler
There is a simple transformation from x,y in one image to x’,y’ in the other one
Simple matrix multiplication+ division
No depth required
p
p’
H

## Slide 125: Roadmap

## Slide 126: Spoiler: simple 2D warp
For each pixel y,x, in output
(x, y)
(x’’, y’)
output (in coordinate system of input 1)
input 2

## Slide 127: Spoiler: simple 2D warp
For each pixel y,x, in output
  (y’,x’,w’)=H -1(y,x,1)
  (y’’, x’’)=(y’/w’ , x’/w’)
  out(y,x)=in(y’’, x’’)
(x, y, 1)
(x’, y’, w’)
(x’/w’, y’/w’)
H-1
matrix multiply
division
output (in coordinate system of input 1)
input 2

## Slide 128: Goal: cut the (3d) middleman

## Slide 129: Questions

## Slide 130: Projective geometry

## Slide 131: Image reprojection: back to 3D
Basic question
  How to relate 2 images from same camera center?
    how to map a pixel from PP1 to PP2
Answer
Cast a ray through each pixel in PP1
Draw the pixel where that ray intersects PP2
But don’t we need to know the geometry
of the two planes in respect to the eye?
Observation:
Rather than thinking of this as a 3D reprojection,
think of it as a 2D image warp from one image to another
      PP1
      PP2

## Slide 132
Don’t rotate stuff, just express in the other coordinate system.

## Slide 133: Simple Perspective Projection
Project all points to the z = 1 plane, viewpoint at the origin:

## Slide 134: Simple Perspective Projection
Project all points to the z = 1 plane, viewpoint at the origin:
Can we represent this with a matrix?
(x’,y’)
(x,y,z)
    x’=x/z
    y’=y/z
z=1
    not directly (division)
    but we can cheat...
    add a third coordinate to the result
      interpret as : we always divide by 3rd coordinate
      see in a few slide...

## Slide 135: 3D rotation
We observe point x, y, z with camera PP1
  first image of our pano
(x’,y’,1)
(x,y,z)
PP1

## Slide 136: 3D rotation
We observe point x, y, z with camera PP1
  first image of our pano
Now we rotate the 3D camera to PP2
  second image of our pano
What is the new 2D projection?
  i.e. where does the a point from the first image reproject into the second one?
(x’,y’,1)
(x,y,z)
PP1
PP2

## Slide 137: 3D rotation
Rotating the camera is the same as rotating the world in the opposite direction
To project a (x,y,z) wrt rotated camera:
  Apply rotation R-1 to (x,y, z)
  Apply projection division
(x’’,y’’, 1)
R(x,y,z)
rotate

## Slide 138: 3D rotation: Pano case
Each image has a different rotation Ri
project (x,y,z) wrt camera rotated by Ri:
  Apply rotation Ri-1 to (x,y, z)
  Apply projection division
Now we understand how to go from the 3D world to individual pano input images
  We now need to go directly from 2D input to another one
(x’’,y’’, 1)
R(x,y,z)
rotate

## Slide 139: Recap
canonical projection = division by z
For other direction, just apply 3D rotation first
  But... this applies only when we know z
    And for panorama stitching, we don’t
    What are we going to do?Are we in big trouble? Should we give up? Buy a 3D scanner? Cancel assignment 6?

## Slide 140: Questions

## Slide 141: Unknown z

## Slide 142: 3D rotation
Now we rotate the 3D camera
What is the new projection?
Rotating the camera is the same as rotating the world in the opposite direction
To project a (x,y,z) wrt rotated camera:
  Apply rotation matrix to (x,y, z)
  Apply projection division
Important: same answer if we rotate (x’, y’, 1) instead!
(x,y,z)
projection plane
(x’’,y’’, 1)

## Slide 143: Points that project on the same x,y
x
z
z=1

## Slide 144: Project to different image?
x
z
z=1

## Slide 145: Rotate
x
z
z=1

## Slide 146: Rotate
x
z
z=1

## Slide 147: Divide by z
x
z
z=1

## Slide 148: Project to different image
x
z
z=1
It doesn’t depend on z
All points that project to the same x,y reproject onto the same x’,y’
  after perspective division

## Slide 149: Back to pano problem
We want to know how points at x,y in the first image get reprojected onto the rotated second image
  problem: we don’t know their z
x
z
z=1

## Slide 150: Back to pano problem
x
z
z=1
We want to know how points at x,y in the first image get reprojected onto the rotated second image
  problem: we don’t know their z
  BUT ID DOESN’T DEPEND ON Z!!!!!!
  LET”S PICK AN ARBITRARY Z=1
(x,y,1)

## Slide 151: Project to different image?
x
z
z=1

## Slide 152: Rotate
x
z
z=1
Apply R to vector (x, y, 1)

## Slide 153: Rotate
x
z
z=1
Apply R to vector (x, y, 1)

## Slide 154: Rotate
x
z
z=1
Apply R to vector (x, y, 1)
divide resulting x’, y’ by resulting z’

## Slide 155: Bottomline
The transformation from one 2D image to a rotated image of the same scene is a 3x3 matrix H applied to x,y,1 followed by a division by z’
  called a homography
Now the only problem is that we usually don’t know H

## Slide 156: Today
The user gives us 4 correspondences
Use regression to compute the matrix

## Slide 157: Questions?

## Slide 158: Homogenous coordinates

## Slide 159: 1D homogeneous coordinates
Add one dimension to make life simpler
(x, w) represent point x/w
x
w
w=1

## Slide 160: Other illustration: 1D homography
Reproject to different line
x
w
w=1

## Slide 161: 1D homography
Reproject to different line
w=1
x
w

## Slide 162: 1D homography
Reproject to different line
Equivalent to rotating 2D points
 reprojection is linear in homogeneous coordinates
  and independent of depth
w=1
x
w

## Slide 163: Camera rotation: unknown z
Same thing but use (x’, y’, 1) instead of (x, y, z)
  Rotate (x’, y’, 1) by R
  Perform division
(x’,y’,1)
(x,y,z)
PP1
PP2

## Slide 164: 3D rotation
Same thing but use (x’, y’, 1) instead of (x, y, z)
  Rotate (x’, y’, 1) by R
  Perform division
Makes sense: depth does not matter, all points along a light ray project to the same point.
  We arbitrarily (but conveniently) choose the point at depth 1
projection plane
R(x’,y’,1)
(x’’,y’’, 1)

## Slide 165: Homogenous coordinates
Representation of 2D points using 3 coordinates
(x, y, w) represents (x/w, y/w)
  Homogenous points are interpreted as Euclidean coordinates by dividing by the last coordinate
Motivations:
  perspective transforms
  Make translations linear
  Duality with hyperplanes.

## Slide 166: Homogeneous coordinate
represent 2D points with 3 numbers
(x, y, w) represents (x/w, y/w)
Allows us to represent projective transforms
Nice thing: projecting onto plane z=1 is just the strict interpretation of homogeneous coordinates
Yes, you can view this as a notation trick
  But math is all about smart notations
Homogenous coordinates are central in computer graphics and machine vision

## Slide 167: Scale invariant
All points (wx, wy, w) for any non-zero w represent the same Euclidean point

## Slide 168: Extra profit
Homogenous coordinates allow us to represent 2D translations as matrices

## Slide 169: Questions?
http://petapixel.com/2013/10/06/beautiful-underwater-panoramas-used-help-scientists-save-coral-reefs/
http://globalreefrecord.org/home_scientific