## Slide 1: Focus, defocus and focal stacks
Frédo Durand
MIT EECS

## Slide 6: Writeup about DSLR vs. mirrorless
https://www.diyphotography.net/the-dslr-will-probably-die-are-mirrorless-the-future-of-large-standalone-cameras/

## Slide 7: Paper on mobile photography
https://www.annualreviews.org/doi/pdf/10.1146/annurev-vision-093019-115521

## Slide 8: Don’t forget the survey on LLMs
https://docs.google.com/forms/d/e/1FAIpQLScJDDd7k4ZVIvwejXMoLyQ3impDdKwDShqyhIpEcd20sWf-WQ/viewform

## Slide 9: Depth of field

## Slide 10: Why you need shallow depth of field
Photo with fake shallow depth of field

## Slide 11: Why you need shallow depth of field
Original photo

## Slide 13: Size of permissible circle?
Assumption on print size, viewing distance, human vision
  Typically for 35mm film: diameter = 0.02mm
Film/sensor resolution (8m photosites for high-end SLR )
Best lenses are around 60 lp/mm (line pair per mm)
Diffraction limit

## Slide 14: Depth of field: Object space
Simplistic view: double cone
  Tells you about the value of one pixel
lens
sensor
Point in focus
Object with texture

## Slide 15: Depth of field: Object space
Simplistic view: double cone
  Only tells you about the value of one pixel
  Things are in fact a little more complicated to assess circles of confusion across the image
  We're missing the magnification factor (proportional to 1/distance and focal length)
lens
sensor
Point in focus
Object with texture

## Slide 16: Circle of confusion
From Basic Photographic Materials and Processes, Stroebel et al.
circle of confusion

## Slide 17: Depth of focus
From Basic Photographic Materials and Processes, Stroebel et al.

## Slide 18: Focusing
Points on focal plane project into a point on sensor plane
lens
focal plane

## Slide 19: Misfocus
Points too far focus too close and project into a circle
  called circle of confusion
lens
focal plane

## Slide 20: Misfocus
Points too far focus too close and project into a circle
  called circle of confusion
lens
focal plane

## Slide 21: Depth of focus: more accurate view
Points too far focus too close and project into a circle
Points too close focus too far and project into a circle
When the circle exceeds a given size, we declare the point out of focus
lens
focal plane

## Slide 22: Depth of focus: more accurate view
Points too far focus too close and project into a circle
Points too close focus too far and project into a circle
When the circle exceeds a given size, we declare the point out of focus
lens
focal plane

## Slide 23: Depth of focus: more accurate view
Max circle of confusion can be achieved in two ways
  point that focuses too close, or too far
The distance between those points is the depth of focus
  Conjugate of depth of field
Depth of focus
lens
focal plane
Depth of field

## Slide 24: Applet demo
http://graphics.stanford.edu/courses/cs178/applets/dof.html

## Slide 25: Bottom line
Depth of field is increased by using a smaller aperture
But lets in less light =>noise
And also diffraction gets worse
Can only be done up to a point
Especially challenging for macro photography
Bottom light: even at smallest possible aperture, often not enough depth of field

## Slide 26: Depth of field calculation

## Slide 27: Depth of focus: more accurate view
Goal: compute depth of field
lens

## Slide 28: Depth of focus: more accurate view
Goal: compute depth of field
  distance d1 and d2 in front and behind the focal plane
  given max circle of confusion
lens
Depth of field
d1
d2

## Slide 29: Depth of focus: more accurate view
Goal: compute depth of field
  distance d1 and d2 in front and behind the focal plane
  given max circle of confusion
Solution: similar triangles
lens
Depth of field
d1
d2

## Slide 30: Depth of focus: more accurate view
Circle of confusion C,
Focusing distance D, focal length f, aperture N
lens
d1
d2
D
~f
C

## Slide 31: Depth of focus: more accurate view
Backproject the circle of confusion diameter C onto the focal plane
  Depends on magnification factor ~ f/D
lens
CD/f
D
~f
C
d1
d2
f/N

## Slide 32: Depth of focus: derivation
lens
CD/f
D
~f
C
d1
d2
f/N

## Slide 33: Depth of focus: more accurate view
lens
CD/f
D
~f
C
d1
d2

## Slide 34: Depth of field: more accurate view
Backproject the image onto the plane in focus
  Backproject circle of confusion
  Depends on magnification factor
Depth of field is slightly asymmetrical
lens
Point in focus
Conjugate of circle of confusion
Depth of field

## Slide 35: Depth of focus: more accurate view
Max circle of confusion can be achieved in two ways
  point that focuses too close, or too far
The distance between those points is the depth of focus
  Conjugate of depth of field
lens
Depth of focus

## Slide 36: Depth of field: more accurate view
Backproject the image onto the plane in focus
  Backproject circle of confusion
  Depends on magnification factor ~ f/D
lens
CD/f
D
C
~f

## Slide 37: Deriving depth of field
Circle of confusion C, magnification m
Simplification: m=f/D
Focusing distance D, focal length f, aperture N
As usual, similar triangles
CD/f
f/N
D
d1
d2

## Slide 38: Deriving depth of field
CD/f
f/N
D-d1
d1

## Slide 39: Deriving depth of field
CD/f
f/N
D
d1
d2

## Slide 40: Deriving depth of field
CD/f
f/N
D
d1
d2
N2C2D2 term can often be neglected when DoF is small (conjugate of circle of confusion is smaller than lens aperture)

## Slide 41: Depth of field and aperture
CD/f
f/N
d1
d2

## Slide 42: Depth of field and aperture
Linear: proportional to f number
Recall: big f number N means small physical aperture
CD/f
f/N
d1
d2

## Slide 43: DoF & aperture
http://www.juzaphoto.com/eng/articles/depth_of_field.htm
f/2.8
f/32

## Slide 44: SLR viewfinder & aperture
By default, an SLR always shows you the biggest aperture
Brighter image
Shallow depth of field help judge focus
Depth of field preview button:
  Stops down to the aperture you have chosen
  Darker image
  Larger depth of field

## Slide 45: Depth of field and focusing distance
Quadratic (bad news for macro) (but careful, our simplifications are not accurate for macro)
f/N
d1
d2
D
CD/f

## Slide 46: Back to Double cone perspective
Recall I said it was simplistic
Seems to say that relationship is linear
But if you add the magnification factor, it's actually quadratic
lens
sensor
Point in focus

## Slide 47: Depth of field & focusing distance
From Photography, London et al.

## Slide 48: Hyperfocal distance
From Basic Photographic Materials and Processes, Stroebel et al.

## Slide 49: Hyperfocal distance
Recall full formula
CD/f
f/N
d1
d2
CD/f

## Slide 50: Hyperfocal distance
When CD/f becomes bigger than f/N
focus at D=f2/NC and sharp from D/2 till infinity
Our other simplifications do not work anymore there: the denominator term has to be taken into account in
CD/f
f/N
d1
d2
CD/f

## Slide 51: Depth of field and focal length
Inverse quadratic: the lens gets bigger, the magnification is higher
CD/f
f/N
D
d1
d2

## Slide 52: Depth of field & focal length
Recall that to get the same image size, we can double the focal length and the distance
Recall what happens to physical aperture size when we double the focal length for the same f number?
  It is doubled
24mm
50mm

## Slide 53: Depth of field & focal length
Same image size (same magnification), same f number
Same depth of field!
Wide-angle lens
Telephoto lens (2x f), same aperture
DoF
DoF

## Slide 54: DoF & Focal length
http://www.juzaphoto.com/eng/articles/depth_of_field.htm
50mm f/4.8
200mm f/4.8 (from 4 times farther)
See also http://luminous-landscape.com/tutorials/dof2.shtml

## Slide 55: Important conclusion
For a given image size and a given f number, the depth of field (in object space) is the same.
  Might be counter intuitive.
  Although only true if assumption respected (far from hyperlocal distance)
Very useful for macro where DoF is critical. You can change your working distance without affecting depth of field
Now what happens to the background blur far far away?

## Slide 56: Important conclusion
For a given image size and a given f number, the depth of field (in object space) is the same.
  The depth of acceptable sharpness is the same
But background far far away looks more blurry Because it gets magnified more
Plus, usually, you don't keep magnification constant

## Slide 57: To learn more
http://toothwalker.org/optics/dof.html
Figure 2. The circle of confusion versus distance at a fixed image magnification for a range of focal lengths.

## Slide 58
Figure 3. A: Gromit photographed with a 100-mm lens at f/4. B: Gromit photographed with a 28-mm lens at f/4. DOF is the same.

## Slide 59: Same object space blur
Figure 4. Background crop from the photographs in Fig. 3. A: 100-mm lens. B: 28-mm lens.

## Slide 60: Good tutorials
http://petapixel.com/2011/05/10/a-detailed-explanation-of-depth-of-field-and-the-factors-that-affect-it/
http://snodart.com/tutorials.php

## Slide 61
Recap

## Slide 62: Effect of parameters
From applied photographic optics
aperture
focusing distance
focal length

## Slide 63: DoF guides
From "The Manual of Photography" Jacobson et al

## Slide 64: Is depth of field good or evil?
It depends, little grasshopper
Want huge DoF: landscape, photojournalists, portrait with environment
Shallow DoF: portrait, wildlife
Steve McCurry
Michael Reichman

## Slide 65: Crazy DoF images
By Matthias Zwicker
The focus is between the two sticks
Sharp version
Really wide aperture version

## Slide 66: Is depth of field a blur?
Depth of field is NOT a convolution of the image
The circle of confusion varies with depth
There are interesting occlusion effects
(If you really want a convolution, there is one, but in 4D space… more about this in ten days)
From Macro Photography

## Slide 67
Sensor size

## Slide 68: Depth of field
It’s all about the size of the lens aperture
lens
sensor
Point in focus
Object with texture
lens
sensor
Point in focus
Object with texture

## Slide 69: Equation
Smaller sensor
  smaller C
  smaller f
But the effect of f is quadratic
Bottom line: the size of the sensor linearly scales the depth of field
  for same field of view, focusing distance and f number (aperture).

## Slide 70: Sensor size
http://www.mediachance.com/dvdlab/dof/index.htm

## Slide 71: The coolest depth of field solution
http://www.mediachance.com/dvdlab/dof/index.htm
Use two optical systems
lens
diffuser
Point in focus
Object with texture
lens
sensor

## Slide 72: The coolest depth of field solution
http://www.mediachance.com/dvdlab/dof/index.htm
lens
diffuser
Point in focus
Object with texture
lens
sensor

## Slide 73: The Frazier lens
The opposite: relay optics for large depth of field in macro shots.
http://photo.stackexchange.com/questions/11124/how-can-a-frazier-lens-achieve-that-massive-dof

## Slide 74: Brenizer method
Simulate larger sensor using panorama stitching
http://www.amazon.com/gp/blog/post/PLNK1UFLDXXBLDMN3

## Slide 75
Seeing through occlusion

## Slide 76: Seeing beyond occlusion
Photo taken through zoo bars
Telephoto at full aperture
The bars are so blurry that they are invisible

## Slide 77: Synthetic aperture
Stanford Camera array (Willburn et al. http://graphics.stanford.edu/papers/CameraArray/)

## Slide 78
Aperture

## Slide 79: Why a bigger aperture
To make things blurrier
  Depth of field
  outside the focal plane
To make things sharper
  Diffraction limit
  on the focal plane
Sharpness & aperture (e.g. for the Canon 50mm f/1.4)
http://www.slrgear.com/reviews/showproduct.php/product/140/sort/2/cat/10/page/3
f/1.4: soft (geometrical aberrations), super shallow Dof. Lots of light!
f/2.8 getting really sharp, shallow depth of field
f/5.6: best sharpness
f/16: diffraction kicks in, loses sharpness. But dpoth of field is big

## Slide 80: Depth of field
More narrow when focusing close
More narrow with bigger sensors
For the same magnification, independent of focal length

## Slide 81
http://petapixel.com/2013/05/17/focus-stacked-macro-photos-of-bugs-by-photographer-nicolas-reusens/

## Slide 82: Focal stack aka Focus stack

## Slide 83: Problem: limited depth of field

## Slide 84: Idea
Take images with different focusing distances
Merge into a full-focus image
  For each pixel, pick sharpest image
  Similar to autofocus
Similar to HDR, panorama
  But along focus dimension
focus
focus
focus

## Slide 85: Evaluating sharpness
Local amount of high-frequency content
green: positive, red: negative
here image focused in the back

## Slide 86: Need for smoothing
The high frequency around an edge goes from positive to negative, through zero
We want high “sharpness” all around the edge
Plus we want spatial coherence in our choice of pixels

## Slide 87: We can’t smooth directly
High frequency has positive and negative values
Local average is zero
By construction: we removed low frequencies!

## Slide 88: Local high frequency energy
Take the square of the high frequencies
  All positive

## Slide 89: Local high frequency energy
Take the square of the high frequencies
  All positive
Take local average using Gaussian filter

## Slide 90: Focal Stack Compositing
Weighted sum of all input images (normalize!)
Each pixel weighted by sharpness value
x
x
x
+
and divide by sum of weights

## Slide 91: Compositing (17 input images)
Weighted sum of all input images
Each pixel weighted by sharpness value

## Slide 92: Compare to single image

## Slide 93: Bells and whistle
So far, simple weights
But we want to give more weight to best image
Potential solution: just use the max
Simpler solution: raise the sharpness to a high exponent (e.g. 4)

## Slide 94: With exponent 1
(The previous version)

## Slide 95: With exponent 4
Subtle difference, but sharper

## Slide 96: Visualization of image weights
Random color for each input image

## Slide 97: Visualization of image weights
Random color for each input image
With exponent =1 : blurrier

## Slide 98: More results: input

## Slide 99: More results: input

## Slide 100: More results: input

## Slide 101: More results: input

## Slide 102: More results: input

## Slide 103: More results: input

## Slide 104: More results: input

## Slide 105: More results: input

## Slide 106: More results: input

## Slide 107: More results: input

## Slide 108: More results: input

## Slide 109: More results: input

## Slide 110: More results

## Slide 111: More results

## Slide 112: More advanced
Choose max image for each pixel
Regularize for spatial coherence
Poisson (gradient) blending
From Agarwala et al.
http://grail.cs.washington.edu/projects/photomontage/

## Slide 113: Focal stack DoF extensions
Capture N images focused at different distances
For each output pixel, choose the sharpest image
  e.g. look at local variance, gradient.

## Slide 114: Focal stack

## Slide 115: Interactive Digital Photomontage

## Slide 116: Compared to our result

## Slide 117: Macro montage
55 images here
Not my code

## Slide 118: How to get the focal stack?
http://www.cognisys-inc.com/stackshot/stackshot.php
Although here we change the viewpoint as well

## Slide 119: Swept under the rug
We also need to scale images
recall that changing the focus changes the field of view / magnification
film
focused
at
infinity
film
focused
close

## Slide 120
Macro

## Slide 121: Scanning: combination in 1 exposure
From Macro photography: Learning from a Master

## Slide 122: Macro is easy with small sensors
1/ minimum focusing distance is way smaller
2/ depth of field is bigger
Summary: you've scaled down the camera, you can take pictures of a scaled-down world
sensor
lens
sensor
Point in focus
Object with texture
lens
Point in focus
Object with texture
Well, except for diffraction (we did not scale wavelength!)

## Slide 123: More
http://grail.cs.washington.edu/projects/photomontage/
http://www.heliconsoft.com/heliconfocus.html
http://people.csail.mit.edu/hasinoff/pubs/hasinoff-timeconstrained-2009.pdf
http://people.csail.mit.edu/hasinoff/pubs/hasinoff-timeconstrained-2009.pdf
http://layersmagazine.com/extended-depth-of-field-with-auto-blend-layers-in-photoshop-cs4.html
http://www1.cs.columbia.edu/CAVE/projects/flexible_dof/images/FocalStack/pool_table/
http://en.wikipedia.org/wiki/Focus_stacking
http://en.wikipedia.org/wiki/Microscopy#Deconvolution
http://www.equisetites.de/palbot/tools/focus_stacking.html
http://www.youtube.com/watch?v=fJiEw4VCcYU
http://www.janrik.net/insects/ExtendedDOF/LepSocNewsFinal/EDOF_NewsLepSoc_2005summer.htm
https://alliance.seas.upenn.edu/~cis581/wiki/Lectures/Pyramid.pdf

## Slide 124: Fake depth of field

## Slide 125: Challenge
Shallow depth of field hard with small sensors
sensor
lens
sensor
Point in focus
Object with texture
lens
Point in focus
Object with texture

## Slide 126: Challenge
Shallow depth of field hard with small sensors
sensor
lens
sensor
Point in focus
Object with texture
lens
Point in focus
Object with texture

## Slide 127
https://people.csail.mit.edu/soonmin/dof/

## Slide 128: Portrait mode
https://research.google/blog/portrait-mode-on-the-pixel-2-and-pixel-2-xl-smartphones/
https://arxiv.org/pdf/1806.04171

## Slide 129
Machine learning-based foreground-background segmentation
Use dual pixels to get a depth map (or analyze local defocus)
Predict desired per-pixel blur radius
Render with non-linear blur (more later)

## Slide 131: Challenge with defocus blur
Remember, not a convolution!
Blur radius depends on input scene depth, not output pixel location
Plus occlusion matters

## Slide 132: *
lens
sensor
Point in focus

## Slide 134: Occlusion
Divide the image into k (=5) depth layers with opacity values
Process each layer independently
Composite back to front (with “over” operator)

## Slide 137: Challenges
Masks are hard, especially around hair!
Need notion of sub-pixel coverage

## Slide 138: Some more recent work
https://arxiv.org/abs/1904.05822
https://imaging.cs.cmu.edu/dual_pixels/