## Slide 1: Fake Depth of Field, Wavefront coding
Frédo Durand
MIT EECS

## Slide 2: De deblurring lecture first

## Slide 3: Is depth of field a blur?
Depth of field is NOT a convolution of the image
The circle of confusion varies with depth
There are interesting occlusion effects
(If you really want a convolution, there is one, but in the light field...)
From Macro Photography

## Slide 4: Fake depth of field

## Slide 5: Challenge
Shallow depth of field hard with small sensors
sensor
lens
sensor
Point in focus
Object with texture
lens
Point in focus
Object with texture

## Slide 6: Challenge
Shallow depth of field hard with small sensors
sensor
lens
sensor
Point in focus
Object with texture
lens
Point in focus
Object with texture

## Slide 7
https://people.csail.mit.edu/soonmin/dof/

## Slide 8: Portrait mode
https://research.google/blog/portrait-mode-on-the-pixel-2-and-pixel-2-xl-smartphones/
https://arxiv.org/pdf/1806.04171

## Slide 9
Machine learning-based foreground-background segmentation
Use dual pixels to get a depth map (or analyze local defocus)
Predict desired per-pixel blur radius
Render with non-linear blur (more later)

## Slide 11: Challenge with defocus blur
Remember, not a convolution!
Blur radius depends on input scene depth, not output pixel location
Plus occlusion matters

## Slide 12: *
lens
sensor
Point in focus

## Slide 14: Occlusion
Divide the image into k (=5) depth layers with opacity values
Process each layer independently
Composite back to front (with “over” operator)

## Slide 17: Challenges
Masks are hard, especially around hair!
Need notion of sub-pixel coverage

## Slide 18: Some more recent work
https://arxiv.org/abs/1904.05822
https://imaging.cs.cmu.edu/dual_pixels/

## Slide 19: Wavefront coding

## Slide 20: Hardware depth of field solution
Stop down! (use smaller aperture)
problem: noise
  http://www.cdm-optics.com/site/publications.php

## Slide 21: Wavefront coding
CDM-Optics, U of Colorado, Boulder
Improve depth of field using weird optics & deconvolution
http://www.cdm-optics.com/site/publications.php
  The worst title ever: "A New Paradigm for Imaging Systems", Cathey and Dowski, Appl. Optics, 2002

## Slide 22: Wavefront coding
Idea: deconvolution to deblur out of focus regions
Sometimes, we can cancel a convolution by another convolution
  This is called deconvolution
Best studied in the Fourier domain (of course!)
  Convolution = multiplication of spectra
  Deconvolution = multiplication by inverse spectrum

## Slide 23: Deconvolution
Assume we know blurring kernel k
f' = f Ä k
 F' = F K (in Fourier space)
Invert by: F=F'/K (in Fourier space)
Well-known problem with deconvolution:
  Impossible to invert for w where K(w)=0
  Numerically unstable when K(w) is small

## Slide 24: Wavefront coding
Idea: deconvolution to deblur out of focus regions
Problem 1: depth of field blur is not shift-invariant
  Depends on depth
  If depth of field is not a convolution, it's harder to use deconvolution ;-(
Problem 2: Depth of field blur "kills information"
  Fourier transform of blurring kernel has low frequency response

## Slide 25: Wavefront coding
Idea: deconvolution to deblur out of focus regions
  Problem 1: depth of field blur is not shift-invariant
  Problem 2: Depth of field blur "kills information"
Solution: change optical system so that
  Rays don't converge anymore
  Image blur is the same for all depth
  Blur spectrum is higher

## Slide 26: Wavefront coding
Idea: deconvolution to deblur out of focus regions
  Problem 1: depth of field blur is not shift-invariant
  Problem 2: Depth of field blur "kills information"
Solution: change optical system so that
  Rays don't converge anymore
  Image blur is the same for all depth
  Blur spectrum is higher
How it's done
  Phase plate (cubic lens z=y3+x3)
  Will do things similar to spherical aberrations

## Slide 27: Ray version

## Slide 28: Image of a point source
aka Point Spread Function (PSF), same as kernel
Normal lens
Wavefront coding
In focus
Out of focus

## Slide 29: Frequency response (MTF)
Magnitude of the Fourier transform of the PSF
Higher is better (noise less amplified by deconvolution)

## Slide 30: Results

## Slide 31: Questions?

## Slide 32: In General: Coded Imaging

## Slide 33: Philosophy: Image capture
A sensor placed alone in the middle of the visual world does not record an image

## Slide 34: Image capture
Pinhole allows you to select light rays

## Slide 35: Image formation: optics
Optics forms an image: selects and integrates light rays

## Slide 36: Image formation: computation
The combination of optics & computation forms the image: selects and combines rays
Generalized optics
Computation
Intermediate optical image
Final
image

## Slide 37: Computational imaging goals
Generalized optics
Computation
Intermediate optical image
Final
image
Better capture information
Form image as a post-process

## Slide 38: Better capture information
Generalized optics
Computation
Intermediate optical image
Final
image
Same as communication theory: optics encodes , computation decodes
Code seeks to minimize distortion

## Slide 39: Form images as a post-process
Generalized optics
Computation
Intermediate optical image
Final
image
The computational part of formation can be done later and multiple times
e.g., enable refocusing

## Slide 40: Lattice focal lens

## Slide 41
Levin et al. 09: assembly of subsquares with different focal powers
each element focuses on a different depth
toy lattice-focal lens with 4 elements
New solution: The lattice-focal lens
32
Notes: Our new lattice focal lens is an assembly of subsquares. The subsquares are cut out of a lenses with different focal power, which means that they focus rays from different depths. In this slide we show a toy lattice focal lens with only 4 subsquares but in practice we have a larger number of sublenses.

## Slide 42
Proof of concept
12 subsquares cut from plano-convex spherical lenses
Attached to main lens
extra focal power needed very low
Modest DOF extension with only 12 subsquares
Hardware construction
36
Notes: We have built a proof-of-concept lattice-focal lens with just 12 elements. By attaching the lattice-focal elements to a high-quality main lens, the focal power we need for each of the subsquares is much lower. This lets us use simple plano-convex glass lenses without suffering from too many aberrations.

## Slide 43
input
depth map
Defocus kernels vary with depth
Depth estimation as for the coded aperture camera [Levin et al. 07]
Depth estimation
defocus kernels at different depths
37
Notes: The defocus kernels of the lattice-focal lens vary with depth. and therefore to process an image we estimate depth in the same way this was done for the coded aperture camera.

## Slide 44
Standard lens reference
38
Notes: Here are real results. This is the input from a standard lens, which has a very shallow depth of field.

## Slide 45
Lattice-focal lens
Notes: And here's an extended-depth of field image produced with our lattice-focal lens.

## Slide 46: Lattice focal lens

## Slide 47
Application: Refocusing from single captured image
44
Notes: The lattice-focal lens provides us with a coarse depth map, and this can be used for post-processing effects. One example is synthetic refocusing from a single image. We can refocus on the back, or any depth in the middle.

## Slide 48
45
Application: Refocusing from single captured image
Notes: .

## Slide 49
46
Application: Refocusing from single captured image
Notes: .

## Slide 50: Depth of field analysis
How do different cameras compare?
What is the best that can be done?

## Slide 51
hello
9
flatworld 1D scene
2D lightfield
a
b
depth
horizontal position
Analysis tool: light field
2 plane parameterization [Levoy and Hanrahan 96]
b plane
a plane
a
b
Notes: If we go through the same exercise for every surface in our toy world, we’ll get the depiction of the lightfield shown here. its dominant characteristics are the slowly varying structures along slopes determined by the object depths, and with faster variations from surface textures in the horizontal direction.
So that’s the lightfield. Now, what do different cameras do, examined in this lightfield domain? studying this gives us insight into the photographic problem.

## Slide 52
hello
10
Pinhole camera
flatworld 1D scene
2D lightfield
depth
horizontal position
a
b
sensor plane
aperture
y =
T
x
b plane
a plane
a
b
Notes: let’s start with the simplest camera, a pinhole camera. we open a very small aperture, and individual light rays pass through the aperture and land on a single sensor element. We’ve color coded each sensor element. Here we show you that operation with our two different parameterizations of the lightfield--the vector-matrix equation form, and in the 2-d form, for better intuition.
We measure only a small part of the lightfield--not much light gets into a pinhole camera. We sample the intensities along a single row of the lightfield, determined by where the aperture lies.

## Slide 53
hello
11
depth
horizontal position
sensor plane
aperture
Lens, focused at green object
flatworld 1D scene
2D lightfield
a
b
y =
T
x
b plane
a plane
a
b
Notes: Now the 2nd simplest camera--a single lens, bringing the sufrace at the b plane into focus at the camera sensor elements. Each sensor element now records all the rays leaving a point at the b plane over the range of a values set by the lens aperture. so each pixel integrates over a vertical swath of the lightfield. We’re recording a lot more of the lightfield, which you can see in each of the 2 lightfield parameterizations depicted here. Because it gives more intuition, from now on, we’ll just show the lightfield in the 2d parameterization.

## Slide 54
hello
12
depth
horizontal position
sensor plane
aperture
Lens, focused at blue object
flatworld 1D scene
2D lightfield
a
b
b plane
a plane
a
b
Notes: let’s change the focus of our lens camera. now it brings points on the surface of the blue object into focus at the detector. so every pixel will integrate over a slanted line in the lightfield space, at the same slope as the blue object.

## Slide 55
hello
13
depth
horizontal position
sensor plane
aperture
Coded aperture lens
flatworld 1D scene
2D lightfield
a
b

## Slide 56
hello
14
depth
horizontal position
apertures
Stereo
flatworld 1D scene
2D lightfield
a
b
sensor plane
b plane
a plane
a
b
Notes: to build more intuition about what cameras record, lets look at some other cameras as patches of integration over the lightfield. a stereo camera has two arrays of lightfield integration patches, offset in a and b according to the baseline of the stereo camera. Here we’re depicting a fixed total number of sensors for each camera, so the spatial resolution of each stereo camera is cut in two.

## Slide 57
hello
15
Plenoptic camera
flatworld 1D scene
2D lightfield
a
b
depth
horizontal position
sensor plane
aperture
Adelson and Wang 92, Ng et al 05
b plane
a plane
a
b
micro-lenses
main lens
Notes: a so-called “plenoptic” camera has a second set of microlenses behind a main lens. placed properly, this allows for both lightray angle as well as position to be recorded, giving a sensing pattern something like that shown schematically here. we measure a lot of angular information, but lose detail in the horizontal dimension.

## Slide 58
hello
16
depth
horizontal position
sensor plane
aperture
Wavefront coding
flatworld 1D scene
2D lightfield
a
b
Dowski and Cathey,94
b plane
a plane
a
b
cubic phase plate
Notes: finally, the lightray integration curves don’t need to be rectilinear patches; they can be curves in the lightfield space as well. One famous camera system that we’ve shown has parabolic lightfield integration paths is wavefront coding. a cubic phase plate leads to the parabolic integration paths, which you can show lead to depth invariant depth-of-focus blur.

## Slide 59: Our new theoretical analysis
http://www.wisdom.weizmann.ac.il/~levina/papers/lattice/
In the 4D light field
  Fourier analysis
Shows that only a 3D subset of the 4D spectrum is useful (dimensionality gap)
Inspires new lens design: lattice-focal lens
Only a 3D subset of the 4D spectrum is useful
Previous designs spend energy outside the useful subset

## Slide 60
The lattice-focal lens focuses on 3D subset
Sliced 2D OTFs at varying depths:
y
x
u
v
4D Fourier Transform
34
Notes: When we increase the number of sublenses the collection of sincs can cover the full focal segment. This is more or less the lens spectrum we wanted- energy over the full focal segment and not outside that segment.

## Slide 61: Comparison of different cameras

## Slide 62
Comparing image reconstruction (simulation)
Object at in-focus depth
standard
lens
coded
aperture
focus
sweep
wavefront
coding
lattice-focal
lens
<
<
<
<
<
Object at extreme depth
35
Notes: Now I show a comparison of computational cameras using synthetic data. We simulate the defocus blur, add Gaussian noise, and deconvolve using Wiener filtering. The first row corresponds to a planar object at the in-focus depth for a standard lens, in the middle of the range. The second row is for the same object at the extreme end of the depth range. The standard lens on the left and the coded aperture to its right capture a perfectly sharp image at the in-focus depth. but for an extreme depth it's so defocused that the reconstruction we get is quite poor, as see in the lower left of the slide. By contrast, the focus sweep camera, wavefront coding and our new lattice-focal lens achieve about the same quality regardless of the depth. Although the standard lens is still better at the in-focus depth, all these computational cameras are much better for out-of-focus depths. As you can see in the rightmost column, the lattice-focal lens achieves the best image quality. This ranking of the designs agrees with the formal spectrum derivations in our paper.

## Slide 63: References
http://www.cdm-optics.com/site/publications.php
http://www.wisdom.weizmann.ac.il/~levina/papers/lattice/
http://www1.cs.columbia.edu/CAVE/publications/pdfs/Nagahara_ECCV08.pdf
http://groups.csail.mit.edu/graphics/CodedAperture/
http://web.media.mit.edu/~raskar/Mask/

## Slide 64: In cell phones
e.g. Nokia E7
Also exploits chromatic aberrations to focus R, G & B at different depths
http://www.allaboutsymbian.com/features/item/12789_EDoF_versus_Auto-focus_Underst.php
http://www.tessera.com/Pages/tessera.aspx
http://www.tessera.com/technologies/imagingandoptics/Documents/OptiML_Focus.pdf

## Slide 65: Other application
Single-image depth sensing
  Blur depends A LOT on depth
  Passive Ranging Through Wave-Front Coding: Information and Application. Johnson, Dowski, Cathey
  http://graphics.stanford.edu/courses/cs448a-06-winter/johnson-ranging-optics00.pdf

## Slide 66: Single image depth sensing

## Slide 67: Important take-home idea
Coded imaging
What the sensor records is not the image we want, it's been coded (like in communication theory)
Image processing decodes it

## Slide 68: Image and Depth from a Conventional Camera with a Coded Aperture
With Anat Levin, Rob Fergus, Bill Freeman [Siggraph 2007]
RGB & coarse depth from single image
Notes: Now let me tell you about computational photography. We design both algorithms and optics to allow you to take better pictures and to get more information with your pictures. For example, we designed a coded aperture where we insert a small binary mask in the middle of a lens, which allows you to depth depth information together with your normal image. Better than that, we can also give you a sharper image without out-of focus regions.

## Slide 69: Coded Aperture: a paradigm of computational photography
Reconstruct light-field / depth
Coding optics, decoding algorithm
Prior on “natural” images (sparse derivative)
Notes: As this work shows, the power of computational photography is in designing both the optics and the algorithm together

## Slide 70: Input
Notes: Here is the kind of image it captures. It’s hard to see at this resolution but the defocus is a little weird.

## Slide 71: Deconvolved (all-focus)
Notes: Now we can use a new deconvolution algorithm we have developed to remove the defocus.

## Slide 72: Depth
Notes: And we get depth information as well.

## Slide 73: Refocusing (from single image!)
Notes: Now with this information, we can do cool things after the fact. We can increase the defocus to get a nice blurry background.

## Slide 74
Refocusing (from single image!)

## Slide 75
Refocusing (from single image!)

## Slide 76
Refocusing (from single image!)

## Slide 77: Results

## Slide 78
Refocusing (from single image!)

## Slide 79
Refocusing (from single image!)

## Slide 80
Refocusing (from single image!)

## Slide 81
    Depth acquisition:
priceless
    50mm f/1.8:
$79.95
    Cardboard:
$1
    Tape:
$1

## Slide 82: Motion-Invariant Photography

## Slide 83
Our counter intuitive solution:
Makes blur invariant to motion- can be removed with spatially uniform deconvolution
- kernel is known (no need to estimate motion)
- kernel identical over the image (no need to segment)
Makes blur easy to invert
To reduce motion blur, increase it!
- move camera as picture is taken
Notes: The solution we propose might sound counter intuitive- to reduce motion blur we increase it. We move the camera during exposure time, so that we also blur the static parts of the scene.
However the motion is designed in a special way which makes blur invariant to object velocity. That means that the entire scene is blurred equally, with a known kernel.
The advantage is that we can remove the blur with a single deconvolution, without any motion estimation and without segmentation.
Another advantage is that our special motion preserve high frequency information and makes the blur easy to invert.

## Slide 84
Motion invariant PSF
integration curves
sheared integration curves
projected PSF
Static
Parabolic
Up to tail clipping, PSF is invariant to slope
Anat Levin, Taeg Sang Cho, Peter Sand, Fredo Durand, William Freeman, SIGGRAPH 2008
Image data
Velocity

## Slide 85
Parabolic sweep
Start by moving very fast to the right
Continuously slow down until stop
Continuously accelerate to the left
Intuition: For any velocity, there is one instant where we track perfectly.
We spend an equal amount of time
tracing each velocity.

## Slide 86
Time 1

## Slide 87
Time 2

## Slide 88
Static camera

## Slide 89
Parabolic motion camera

## Slide 90
Comparing camera reconstruction
Note: synthetic rendering, exact PSF is known
Static
Flutter Shutter
Parabolic
Blurred input
Deblurred output
Notes: Here is a visual comparison. We synthetically blurred a scene according to all 3 camera models and add an equal amount of noise. The inversion of a static camera blur is worst, a flutter shutter model does better, but the parabolic motion preserves much more information.

## Slide 91
For each spatial frequency, max budget across velocity range
Upper bound given velocity range
Primal Domain
t
x
Frequency Domain
t
x
Objects
Camera integration curve
Frequencies from possible motions
?
Notes: In each column the best thing to do is to distribute the bounded budget uniformly within the wedge.
Therefore we end up with an upper bound on the optimal power spectrum that we can hope to achieve.

## Slide 92
slope wedge
slope wedge
slope wedge
slope wedge
Cameras and information preservation
Static
Flutter shutter
Parabolic
Upper bound
Bounded “budget” per column
Constant horizontally
Spends frequency “budget” outside wedge
Handles 2D motion
Near optimal “budget” usage at all frequencies
Notes: Now let’s see how different cameras do with respect to this upper bound.
We note that the power spectrum of a flutter shutter camera must be constant horizontally. Therefore it must spend budget outside the wedge. Since the norm of each column is bounded, this means less budget for the desired velocities range.
In contrast to this, the power spectrum of the parabolic curve fits the wedge shape and does not spend much budget outside the wedge.
In fact, in the paper we prove that it is getting very close to the optimal upper bound.

## Slide 93
Experimental set-up
Ideally move sensor (requires same hardware as existing stabilization systems)

## Slide 94
Linear rail
Our parabolic input- Blur is invariant to velocity
Static camera input-Unknown and variable blur
Notes: We move to some real results.
Here is an image from a static camera- the scene contains multiple depth layers which translate into multiple motion velocities.
In contrast, here is the input from our camera. It is blurred everywhere, but blurred equally everywhere.

## Slide 95
Linear rail
Static camera input-Unknown and variable blur
Our output after deblurring- NON-BLIND deconvolution
Notes: Therefore we can remove the blur with single uniform deconvolution without estimating the motion or segmenting the image.
One can notice some information loss at the static background but the moving parts are significantly improved.
The objects in this scene were moving on a perfect linear rail.

## Slide 96
Input from a static camera
Input from our parabolic camera- identical blur over both static and moving parts
Deblurred output- entire image deblurred with identical known PSF, no segmentation and no motion estimation

## Slide 97: Comp Photo @MIT

## Slide 98: Computational Imaging at MIT
Ted Adelson (BCS)
George Barbastathis (Mechanical Engineering)
Fredo Durand (EECS)
Bill Freeman (EECS)
Berthold Horn (EECS)
Wojciech Matusik (EECS)
Ramesh Raskar (Medialab)